## Slide 1
OPTIMIZING FIRST PASS YIELD
AN Automated Pressure & Vacuum Monitoring System for TRI ICT Machines To Prevent False Call During Vacuum & pneumatic
Technical Specifications & Operational Architecture Documentation

## Slide 2
The Problem: Unnoticed Pneumatic & vacuum Fluctuations
02. Fixtures Lose Pull-Down Force
Pogo pins fail to make proper contact with test pads, causing unstable connection pathways.
01. False Failures (False Calls)
Good Devices Under Test (DUTs) are flagged as failed due to open circuit faults.
03. Component & Pin Damage
Incomplete seal pressure leads to misaligned pin contact and rapid trace/pin wear.

## Slide 3
Solution Architecture: Hardwired Safety Interlock
Zero Software Failure Points: No PLC or Microcontroller Required
This system implements a hardwired hardware safety interlock using SMC Digital Pressure Switches operating in Window Comparator Mode connected directly to 24V DC switching relays.
Logical Hardware Signal Flow Chain:
• Positive Air Line Supply: Monitored by SMC ISE20 switch → Actuates Relay CR1 (NO Contact in Series)
• Vacuum Line Suction Level: Monitored by SMC ZSE20 switch → Actuates Relay CR2 (NO Contact in Series)
• Series Output Validation: ICT Start Enable Signal passes ONLY when both are OK. Otherwise triggers Failsafe Alert (Red Light/Buzzer).

## Slide 4
Operational Thresholds & Window Ranges
Parameter | Sensor Model | Window Range Limit | Signal Output Logic
Main Air Supply | SMC ISE20 | 4.0 to 6.0 kg/cm² (4 to 6 bar) | Active-HIGH (24 V) when inside window limits
Fixture Vacuum | SMC ZSE20 | -16 to -25 cmHg (Approx. -20 to -33 kPa) | Active-HIGH (24 V) when inside window limits
Failsafe Drop-out Logic:
Both sensors output 24 V (Active-HIGH) only while their inputs remain inside the specified window. If either reading drifts outside its range, the corresponding relay (CR1 / CR2) drops out, the series interlock opens, and the ICT start enable is completely blocked.

## Slide 5
SMC ISE20 Positive Pressure Switch Specifications
Input Technical Specifications
• Power Supply Voltage: 12–24 V DC ±10% (ripple p-p 10% max)
• Current Consumption: ≤ 25 mA
• Applicable Fluid Type: Air, non-corrosive / non-flammable gas
• Rated Pressure Scope: -0.100 to 1.000 MPa (positive pressure)
Output & Control Technical Specifications
• Output Topology: NPN or PNP open collector, 1 output channel
• Configurable Modes: Hysteresis, window comparator, error, or OFF
• Max Load Capacity: 80 mA maximum
• Max Applied Volt: 28 V (for NPN open collector configurations)
• Internal Volt Drop: ≤ 1 V (measured at full 80 mA load)
• Response Delay Time: ≤ 1.5 ms (Anti-chatter: 20–5,000 ms selectable)

## Slide 6
SMC ZSE20 Vacuum Pressure Switch Specifications
Input Technical Specifications
• Power Supply Voltage: 12–24 V DC ±10% standard tracking
• Current Demands: ≤ 25 mA (ZSE20); ≤ 35 mA (ZSE20B)
• Applicable Fluid Type: Air, non-corrosive / non-flammable gas
• Rated Vacuum Scope: 0.0 to -101.0 kPa (vacuum threshold)
Output & Configuration Specifications
• Available Output Types: ZSE20: 1 output; ZSE20B: 2 outputs + analog
• Output Configurations: NPN or PNP open collector choices
• Max Load Current: 80 mA maximum
• Max Applied Volt: 28 V (for NPN open collector loops)
• Internal Volt Drop: ≤ 1 V (measured at full 80 mA load)
• High-Speed Response: ≤ 1.5 ms delay time for sharp control loop